## Slide 1
GRaD-Nav Real4Real audit
AirLab / 8 October 2026
1
Tested dynamics component
Rendering and policy remain blocked
One existing A6000 host. No training. Instance remains running.
Decision: reuse dynamics for research diagnostics. Defer the complete Real4Real workflow.
Notes: Evidence: https://github.com/WorldExplored/R4R-Sims/tree/audit/grad-nav/results/grad-nav/. Exact source refs: docs/grad-nav/sources.md. All source/runtime failures are retained.

## Slide 2
Real4Real evidence still needed
AirLab / 8 October 2026
2
Outdoor residential, suburban and campus scenes below 100 m
Held-out horizontal and vertical camera trajectories
Capture at 15 m and rendering at 50 m remains a research question
Sparse capture coverage and sparse physical content need separate tests
Notes: Evidence: https://github.com/WorldExplored/R4R-Sims/tree/audit/grad-nav/results/grad-nav/. Exact source refs: docs/grad-nav/sources.md. All source/runtime failures are retained.
Project context: docs/r4r-audit-context.md. No AirLab calibrated held-out assets were supplied.

## Slide 3
Action, state and observation path
AirLab / 8 October 2026
3
Requested
action
Dynamics
Achieved
state
Camera
mount
Gaussian
renderer
RGB and
depth
B: measured
Algebra checked
A/D: blocked
C needs the original actor, normalization, VAE and trained visual observation components.
Notes: Evidence: https://github.com/WorldExplored/R4R-Sims/tree/audit/grad-nav/results/grad-nav/. Exact source refs: docs/grad-nav/sources.md. All source/runtime failures are retained.
B executes direct dynamics. Transform checks execute exact baseline helpers. A and D fail before a rendered image. Native actor/CENet omitted, never replaced with random outputs.

## Slide 4
Released scene assets recovered
AirLab / 8 October 2026
4
README file IDs returned 404. The author folder supplied replacement IDs.
Gaussian archive 5.049 GB. Full expanded size 5.827 GB.
Point-cloud archive 0.294 GB. Selected cloud 65.9 MB.
Selected gate_mid inputs: 1.140 GB across 1,213 locally verified files.
Notes: Evidence: https://github.com/WorldExplored/R4R-Sims/tree/audit/grad-nav/results/grad-nav/. Exact source refs: docs/grad-nav/sources.md. All source/runtime failures are retained.
Author Drive replacement IDs and archive SHA256 are in asset-inventory.csv and results/grad-nav/preflight/download-hashes.json. Scene terms remain unverified.

## Slide 5
B feedback response
AirLab / 8 October 2026
5
Chart: Height (m)
Final error
0.0356 m
Overshoot
0.1030 m
First 0.02 m band entry
1.25 s
The error band is an authored diagnostic. First entry does not establish settling or stable hover.
Notes: Evidence: https://github.com/WorldExplored/R4R-Sims/tree/audit/grad-nav/results/grad-nav/. Exact source refs: docs/grad-nav/sources.md. All source/runtime failures are retained.
20261009T012429Z-recovery-e58f8a state.jsonl. kp=2 N/m, kd=0.8 N/(m/s), target1.25m, initial1.0m. Direct normalized thrust and zero rates, noise0. Timing/geometry are simulation diagnostics.

## Slide 6
B scope and measured behavior
AirLab / 8 October 2026
6
Force balance: 20 × 0.05 s. Height 1.25 m, drift 0.0 at float32 precision.
Feedback: kp 2, kd 0.8. Initial perturbation −0.25 m.
One second: drift +0.1706 m, remaining error 0.0794 m, no overshoot.
Five seconds: drift +0.2144 m, error 0.0356 m, overshoot 0.1030 m.
No saturation. Dynamics median about 14.2 ms, with GPU synchronization. Rendering and policy latency unmeasured.
Notes: Evidence: https://github.com/WorldExplored/R4R-Sims/tree/audit/grad-nav/results/grad-nav/. Exact source refs: docs/grad-nav/sources.md. All source/runtime failures are retained.
Force/smoke/recovery metrics.json, config.json and action/state records. No visual policy or native delay/filter/contact logic.

## Slide 7
Numerical camera checks
AirLab / 8 October 2026
7
Camera helper uses xyzw. Dynamics uses wxyz. Conflicting comments are recorded.
Identity, 90° yaw and translation composition checks passed.
Active helper applies no dataparser normalization. Scale/alignment needs scene validation.
Rounded mount orthonormality residual: 0.00042425.
These are algebraic checks. No rendered-camera equivalence or visual calibration was established.
Notes: Evidence: https://github.com/WorldExplored/R4R-Sims/tree/audit/grad-nav/results/grad-nav/. Exact source refs: docs/grad-nav/sources.md. All source/runtime failures are retained.
20261009T012433Z-conversion-04f90b/conversion.json and pinned gs_local.py. Loaded camera metadata recorded in failed A attempts.

## Slide 8
Rendering failure and repair history
AirLab / 8 October 2026
8
gcc: fatal error: cannot execute ‘cc1plus’:
execvp: No such file or directory
nvcc then failed to preprocess host compiler properties.
nvcc 11.8.89. Default gcc 12.3.0. g++ 11.4.0.
cc1plus exists under /usr/lib/gcc/x86_64-linux-gnu/11/.
Two adapter repairs: checkpoint root, scalar camera shape.
Launch correction exposed installed Ninja. A/D remain blocked.
Notes: Evidence: https://github.com/WorldExplored/R4R-Sims/tree/audit/grad-nav/results/grad-nav/. Exact source refs: docs/grad-nav/sources.md. All source/runtime failures are retained.
repair-history.json. A final20261009T013743Z-a-b58f3b and D final20261009T013759Z-d-1ca173 console logs. No additional compiler/package repair after user stop.

## Slide 9
Native policy and collision limits
AirLab / 8 October 2026
9
C blocked: scene checkpoints do not supply the original six learned components.
The native body-rate termination check reads quaternion fields 10:13.
Obstacle handling uses forward-FOV nearest-point distance and reward.
Rear and coincident synthetic points returned infinity. No body-volume contact test.
Notes: Evidence: https://github.com/WorldExplored/R4R-Sims/tree/audit/grad-nav/results/grad-nav/. Exact source refs: docs/grad-nav/sources.md. All source/runtime failures are retained.
Pinned drone_long_traj.py:777 reads privileged10:13. Quaternions9:13, rates13:16. point_cloud_util.py FOV diagnostics. GradNav.load six-object schema.

## Slide 10
Outdoor fidelity remains untested
AirLab / 8 October 2026
10
No PSNR, SSIM or LPIPS result. No validated held-out reconstruction split.
No altitude-change, sparse-capture, vegetation or moving-object experiment.
Indoor/gate paper results motivate study. Outdoor and racing were not executed.
Other candidate scenes, controllers and hardware differ. No matched ranking.
Notes: Evidence: https://github.com/WorldExplored/R4R-Sims/tree/audit/grad-nav/results/grad-nav/. Exact source refs: docs/grad-nav/sources.md. All source/runtime failures are retained.
Dataset transforms/config are preserved, but prior reconstruction/fitting exclusion is not attested. Comparisons read from recorded Project AirSim, Unreal and TravelUAV branch SHAs.

## Slide 11
Decision, preservation and next evidence
AirLab / 8 October 2026
11
Reuse the tested dynamics component. Defer GRaD-Nav as the complete Real4Real workflow.
All 11 run directories and 1,213 scientific files verified locally.
Logs, configs, route records and compiler failures are preserved.
Later: targeted host-compiler selection, rendered-camera validation, original policy components and trusted held-out real capture.
Notes: Evidence: https://github.com/WorldExplored/R4R-Sims/tree/audit/grad-nav/results/grad-nav/. Exact source refs: docs/grad-nav/sources.md. All source/runtime failures are retained.
artifact-index.md, preservation.json, sources.md and handoff.md. Original phase1 retained with hashes. No unrelated files/environments/drivers/processes changed. Instance remains running.

## Slide 12
Provenance appendix
AirLab / 8 October 2026
12
Upstream baseline: d9b00e16107338e49071c65f44582c013e522633
Current source inspected: 95218abe9a5d355519cdaab78d915365303066fe
Host: Ubuntu 22.04.5, RTX A6000, 6 vCPU, 47 GiB RAM
Rendering stack: Torch 2.1.2/cu118, NS 1.1.3, gsplat 1.0.0.
Full-instance charges unknown. $0.54/hour is an unconfirmed GPU-only quote. No termination or cleanup occurred.
Notes: Evidence: https://github.com/WorldExplored/R4R-Sims/tree/audit/grad-nav/results/grad-nav/. Exact source refs: docs/grad-nav/sources.md. All source/runtime failures are retained.
Full upstream lines and asset digests in sources.md, asset-inventory.csv and repair-history.json. See repository artifact index for each run.